## Slide 1: Industrial Cold Chain Storage System (IoT)
Real-time Vaccine & Food Safety Monitoring
Name: [Your Name]
Course: IoT Systems
Date: 12-01-2022

## Slide 2: Introduction & Problem Statement
The Problem:
- Vaccines and perishable food spoil if temperatures fluctuate.
- Manual monitoring is slow, prone to error, and expensive.
- Power failures can destroy millions in inventory.
The Goal:
- Automate monitoring using IoT sensors (MQTT).
- Provide real-time 'Critical Alarms' with audio feedback.
- Ensure data persistence (SQLite) for safety compliance.

## Slide 3: High-Level System Architecture
[Insert Block Diagram Here]
Architecture Flow:
1. Producers (Edge): Emulators for Vaccine/Food Units & Power.
2. Broker (Transport): HiveMQ / Local MQTT Broker.
3. Consumer (Brain): Manager.py processes logic & alarms.
4. Storage (Persistence): Local SQLite Database.
5. Interface (UI): PyQt5 GUI for real-time dashboard.

## Slide 4: Design Concept & Technologies
Communication Protocol: MQTT
- Chosen for lightweight, real-time, decoupled communication.
Tech Stack:
- Language: Python 3
- Connectivity: paho-mqtt
- GUI: PyQt5
- Database: sqlite3
- Alerts: winsound (Audio Feedback)

## Slide 5: Main Modules: The Emulators
Simulating a distributed warehouse environment:
1. Vaccine_Unit (Target -20°C): Critical threshold monitoring.
2. Food_Unit (Target 4°C): Standard cold storage.
3. Main_Power (kW): Monitors infrastructure health.
4. Backup_Cooler: Actuator that triggers automatically on alarm.

## Slide 6: Main Modules: Manager & Database
The Manager (Manager.py):
- Subscribes to topic 'pr/Smart/#' (Wildcard).
- Analyzes incoming payloads against safety rules.
- Publishes commands (e.g., turn ON backup).
The Database (SQLite):
- Tables: 'iot_devices' (State) and 'data' (History).
- Stores timestamp, device_ID, and value for auditing.

## Slide 7: Case 1: Critical Alarm Loop
Scenario: Vaccine Unit fails, Temp rises > -15°C
The Automated Flow:
1. Sensor publishes high temp (-14°C).
2. Manager detects violation -> Publishes 'CRITICAL ALARM'.
3. Manager sends 'ON' command to Backup Cooler.
4. GUI receives Alarm -> Plays Sound -> Flashes Warning.
5. Backup Cooler activates to restore safety.

## Slide 8: Case 2: Power Failure Detection
Scenario: Main Power drops below 0.1 kW
The Infrastructure Flow:
1. Meter Emulator reports 0.0 kW.
2. Manager identifies total power loss.
3. Manager triggers 'POWER FAILURE ALARM'.
4. System alerts operators immediately via Audio to check generators.

## Slide 9: Live Demonstration
[Insert Video or Switch to Live App]
Demonstration Checklist:
- Launching the System (Batch file).
- Nominal Operation (Green Status).
- Manual Trigger: Forcing Vaccine Unit Temp UP.
- Hearing the Alarm Sound.
- Seeing the Backup Cooler Activate.

## Slide 10: Summary & IoT Implementation
Project Topic: Solved unmonitored cold storage risks.
IoT Broker Usage:
- Central message bus decoupling sensors from the dashboard.
- Allowed for independent scaling of sensors.
Device/Protocol Usage:
- Emulated edge devices with independent logic.
- Utilized MQTT Topics (pr/Smart/...) for efficient filtering.

## Slide 11: Conclusions
Key Takeaways:
1. Real-time alerts significantly reduce reaction time.
2. Local database ensures data ownership and reliability.
3. Modular architecture allows easy addition of new zones.
Future Improvements:
- Cloud integration for remote mobile alerts.
- Predictive maintenance using ML on the SQLite data.

## Slide 12: Bibliography & Appendix
Sources:
- Eclipse Paho MQTT Documentation
- PyQt5 Reference Guide
- Course Lectures (IoT Protocols)
Appendix:
- Link to GitHub Repository: [Insert Link]
- Full Source Code attached in Moodle submission.